## Slide 1: P&S Modern SSDs Basics of NAND Flash-Based SSDs
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
12 October 2022

## Slide 2: Today’s Agenda
SSD Organization & Request Handling
NAND Flash Organization
NAND Flash Operations
SSD Organization & Request Handling
NAND Flash Organization
NAND Flash Operations

## Slide 3: Modern SSD Architecture
A modern SSD is a complicated system that consists of multiple cores, HW controllers, DRAM, and NAND flash memory packages
Samsung PM853T 960GB Enterprise SSD (from https://www.tweaktown.com/reviews/6695/samsung-pm853t-960gb-enterprise-ssd-review/index.html)
Core
Core
Core
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
Request Handler
ECC/Randomizer
Encryption Engine
SSD Controller
NAND Packages
8×128 GB = 1 TB
LPDDR DRAM
0.001×1,024 = 1 GB

## Slide 4
Another Overview
Host Interface Layer (HIL)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
4

## Slide 5
Flash Translation Layer (FTL)
Request Handling: Write
Data Cache Management
Address Translation
GC/WL/Refresh/…
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
Host Interface Layer (HIL)
DRAM
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
Communication with the host operating system (receives & returns requests)
  Via a certain interface (SATA or NVMe)
A host I/O request includes
  Request direction (read or write)
  Offset (start sector address)
  Size (number of sectors)
  Typically aligned by 4 KiB
5

## Slide 6
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
Buffering data to write (read from NAND flash memory)
  Essential to reducing write latency
  Enables flexible I/O scheduling
  Helpful for improving lifetime (not so likely)
Limited size (e.g., tens of MBs)
  Needs to ensure data integrity even under sudden power-off
  Most DRAM capacity is used for L2P mappings
Flash Translation Layer (FTL)
Address Translation
GC/WL/Refresh/…
Write Buffer
Data Cache Management
6

## Slide 7
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Metadata (e.g., P/E Cycles)
Host Request Queue
Core functionality for out-of-place writes
  To hide the erase-before-write property
Needs to maintain L2P mappings
  Logical Page Address (LPA)  Physical Page Address (PPA)
Mapping granularity: 4 KiB
  4 Bytes for 4 KiB  0.1% of SSD capacity
Flash Translation Layer (FTL)
GC/WL/Refresh/…
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
7

## Slide 8
Host Interface Layer (HIL)
Request Handling: Write
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Host Request Queue
Garbage collection (GC)
  Reclaims free pages
  Selects a victim block  copies all valid pages  erase the victim block
Wear-leveling (WL)
  Evenly distributes P/E cycles across NAND flash blocks
  Hot/cold swapping
Data refresh
  Refresh pages with long retention ages
Flash Translation Layer (FTL)
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
GC/WL/Refresh/…
Metadata (e.g., P/E Cycles)
8

## Slide 9
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Host Interface Layer (HIL)
Request Handling: Write
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
Randomizer
  Scrambling data to write
  To avoid worst-case data patterns that can lead to significant errors
Error-correcting codes (ECC)
  Can detect/correct errors: e.g., 72 bits/1 KiB error-correction capability
  Stores additional parity information together with raw data
Issues NAND flash commands
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
9

## Slide 10
Host Interface Layer (HIL)
Request Handling: Read
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Host Request Queue
First checks if the request data exists in the write buffer
  If so, returns the corresponding request immediately with the data
A host read request can be involved with several pages
  Such a request can be returned only after all the requested data is ready
Flash Translation Layer (FTL)
Address Translation
GC/WL/Refresh/…
Write Buffer
Data Cache Management
10

## Slide 11
Host Interface Layer (HIL)
Request Handling: Read
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
DRAM
Metadata (e.g., P/E Cycles)
Host Request Queue
Finds the PPA where the request data is stored from the L2P mapping table
Flash Translation Layer (FTL)
GC/WL/Refresh/…
Write Buffer
Data Cache Management
Address Translation
Logical-to-Physical Mappings
11

## Slide 12
DRAM
Host Request Queue
Write Buffer
Logical-to-Physical Mappings
Metadata (e.g., P/E Cycles)
Flash Translation Layer (FTL)
Data Cache Management
Address Translation
GC/WL/Refresh/…
Host Interface Layer (HIL)
Request Handling: Read
First reads the raw data from the flash chip
Performs ECC decoding
Derandomizes the raw data
ECC decoding can fail
  Retries reading of the page w/ adjusted VREF
Flash Controller
ECC
Randomizer
CTRL
CTRL
…
12
NAND
Flash
Package
NAND
Flash
Package
NAND
Flash
Package
…
…

## Slide 13: Today’s Agenda
SSD Organization & Request Handling
NAND Flash Organization
NAND Flash Operation

## Slide 14: A Flash Cell
Basically, it is a transistor
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
ID
VTH
(Threshold Voltage)
VGS >VTH
VGS < VTH

## Slide 15: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)

## Slide 16: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VPGM = 20 V
GND
–
–
–
–
Tunneling

## Slide 17: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
  Changes the cell’s threshold voltage (VTH)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VTH'
Tunneling
GND
20 V
–
–
–
–
VREF
VTH < VREF
VTH > VREF
‘1’
‘0’

## Slide 18: Flash Cell Characteristics
Multi-leveling: A flash cell can store multiple bits
Retention loss: A cell leaks electrons over time
Limited lifetime: A cell wears out after P/E cycling
Flash Cell
Program:
Inject electrons
Erase:
Eject electrons
11
01
00
10
2-bit Multi-level Cell
1 year
1 year
11
01
00
10
11
01
00
10
11
01
00
10
00
Retention error!
1 year
@ 1K P/E cycles
1 year
@ 10K P/E cycles
11
01
00
10
11
01
00
10
00
Retention error!
11
01
00
10

## Slide 19: A NAND String
Multiple (e.g., 128) flash cells are serially connected
…
Bitline (BL)
VPASS
(> 6V)
VPASS
VPASS
Target Cell
…
Bitline (BL)
NAND String

## Slide 20: Pages and Blocks
A large number (> 100,000) of cells operate concurrently
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
…
WL0
Wordline
WL1
WL126
WL127
…
…
…
…
Page = 16 + α KiB
Block = {(# of WL)×(# of bits per cell)} pages

## Slide 21: Pages and Blocks (Continued)
Program and erase: Unidirectional
  Programming a cell  Increasing the cell’s VTH
  Eraseing a cell  Decreasing the cell’s VTH
Programming a page cannot change ‘0’ cells to ‘1’ cells  Erase-before-write property
Erase unit: Block
  Increase erase bandwidth
  Makes in-place write on a page very inefficient  Out-of-place write & GC

## Slide 22: Planes
A large number (> 1,000) of blocks share bitlines in a plane
…
BL0
BL0
BL1
BL2
BL132,095
…
…
…
…
WL0
WL1
WL126
WL127
Block0
Block1
Block2
Block2,047
…

## Slide 23: Planes
A large number (> 1,000) of blocks share bitlines in a plane
…
BL0
WL0
WL1
WL126
WL127
SSL
GSL
String Select Line
Ground Select Line
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…

## Slide 24: Planes and Dies
A die contains multiple (e.g., 2 – 4) planes
A 21-nm 2D NAND Flash Die
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Row/Column Decoders
Plane0
Planes share decoders: limits internal parallelism (only operations @ the same WL offset)

## Slide 25: Today’s Agenda
SSD Organization & Request Handling
NAND Flash Organization
NAND Flash Operation

## Slide 26: Threshold Voltage Distribution
VTH distribution of cells in a programmed page/block/chip
Why distribution? Variations across the cells
  Some cells are more easily programmed or erased
# of cells
Erased (E)
0
Programmed
1
VREF
Threshold voltage (VTH)
y
x
There are y cells whose VTH = x V

## Slide 27: VTH Distribution of MLC NAND Flash
Multi-level cell (MLC) technique
  2m VTH states required to store m bits in a single flash cell
Limited width of the VTH window: Need to
  Make each VTH state narrow
  Guarantee sufficient margins b/w adjacent VTH states
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
margin
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 28: VTH Distribution of MLC NAND Flash
Multi-level cell (MLC) technique
  2m VTH states required to store m bits in a single flash cell
Limited width of the VTH window: Need to
  Make each VTH state narrow
  Guarantee sufficient margins b/w adjacent VTH states
    VTH changes over time after programmed
    Narrower margins  Lower reliability
    More bits per cell  higher density but lower reliability
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
margin
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
Shifted & widened after programmed
Error cells

## Slide 29: Basic Operation: Page Program
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
SSL
Wordline
WLk-1
WLk
GSL
…
…
…
…
Target Page
Block
WLk+1
…
…
…
…
…
…
String Select Line
Ground Select Line

## Slide 30: Basic Operation: Page Program
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
SSL
Wordline
WLk-1
WLk
GSL
…
…
…
…
WLk+1
…
…
…
…
…
…
String Select Line
Ground Select Line
WL control – All other cells operate as a resistance
VCC
VPASS
VPROG
VPASS
VCC

## Slide 31: Basic Operation: Page Program
BL control – Inhibits cells to not be programmed
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit

## Slide 32: Basic Operation: Page Program
BL control – Inhibits cells to not be programmed
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND

## Slide 33: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)

## Slide 34: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
0
Programmed
1
VREF
Threshold voltage (VTH)
Inhibited cells
Programmed cells

## Slide 35: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Hard-to-program cells
Easy-to-program cells

## Slide 36: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG0
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Verified as programmed

## Slide 37: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells

## Slide 38: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG1
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells

## Slide 39: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG1
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells
Programmed
0

## Slide 40: Basic Operation: Page Read
WL control – All other cells operate as a resistance
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0

## Slide 41: Basic Operation: Page Read
BL control – Charge all BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
To Vcc
To VCC
To VCC
To VCC
To VCC
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0

## Slide 42: Basic Operation: Page Read
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
0 (No current)
1 (Current)
0
1
0
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0
VTH < VREF
VTH > VREF

## Slide 43: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 44: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 45: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 46: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 47: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
000
1
1
0
0
1
VREF5
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 48: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
1
1
0
0
1
VREF5
1
1
0
0
1
VREF3
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 49: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
1
1
0
0
1
VREF5
1
1
0
0
1
VREF3
1
0
0
0
1
VREF1
1
0
0
0
1
XOR
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 50: Basic Operation: Page Read – Takeaways
MLC NAND flash memory requires an on-chip XOR logic
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 51: Basic Operation: Page Read – Takeaways
MLC NAND flash memory requires an on-chip XOR logic
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 52: Basic Operation: Page Read – Takeaways
MLC NAND flash memory requires an on-chip XOR logic
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 53: Basic Operation: Page Read – Takeaways
MLC NAND flash memory requires an on-chip XOR logic
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 54
Required Material
54
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, “Errors in Flash-Memory-Based Solid-State Drives: Analysis, Mitigation, and Recovery,” Invited Book Chapter in Inside Solid State Drives, 2018 - Introduction and Section 1
Jisung Park, Myungsuk Kim, Myoungjun Chun, Lois Orosa, Jihong Kim, and Onur Mutlu, “Reducing Solid-State Drive Read Latency by Optimizing Read-Retry,” In ASPLOS, 2021

## Slide 55
Recommended Material
55
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose, Jeremie Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi, Lois Orosa, Juan Gómez Luna, and Onur Mutlu, “FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives,” In ISCA, 2018

## Slide 56: P&S Modern SSDs Basics of NAND Flash-Based SSDs
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
12 October 2022

## Slide 57: P&S Modern SSDs Projects

## Slide 58: Background
Key Observation 1: A two-input AND operation can be performed by reading two wordlines simultaneously in the same NAND string
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…
WL127
WL126
…
NAND String
1
0
1
1
WL0
WL1
BL0
A
B
A•B
2-input AND

## Slide 59: Background
Key Observation 2: A two-input OR operation can be performed by reading a wordline simultaneously from two NAND strings connected to the same bitline
BL0
BL1
BL2
BL132,095
…
…
…
…
Block0
Block1
Block2
Block2,047
…
WL127
WL126
…
NAND String
1
0
1
1
WL0
WL1
BL0
2-input OR
A
B
A+B

## Slide 60: Multi-Wordline Sensing (MWS)
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise AND is performed on multiple wordlines in the same NAND string
BL1
⋯
⋯
⋯
WLm
1
⋯
1
WLc
WLa
Result
WLb
1
1
Target Cells
Unread Cell
WLa AND WLb AND WLc

## Slide 61: Multi-Wordline Sensing (MWS)
1
Unread Cell
BL activation
BL1
⋯
⋯
⋯
WLm
1
⋯
1
WLc
WLa
WLb
1
1
WLa AND WLb AND WLc
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise AND is performed on multiple wordlines in the same NAND string
Activate WL
Activate WL
Activate WL
Result

## Slide 62: Multi-Wordline Sensing (MWS)
1
Unread Cell
BL activation
BL1
⋯
⋯
⋯
WLm
1
⋯
1
WLc
WLa
WLb
1
1
Target Cells
WLx AND WLy AND WLz
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise AND is performed on multiple wordlines in the same NAND string
Result
Unread Cell
BL2
⋯
⋯
⋯
WLw
1
⋯
1
WLz
WLx
WLy
1
Target Cells
0
Result
WLa AND WLb AND WLc

## Slide 63: Multi-Wordline Sensing (MWS)
1
Unread Cell
BL activation
BL1
⋯
⋯
⋯
WLm
1
⋯
1
WLc
WLa
WLb
1
1
Target Cells
0
Unread Cell
BL activation
BL2
⋯
⋯
⋯
WLw
1
⋯
1
WLz
WLx
WLy
1
0
WLa AND WLb AND WLc
WLx AND WLy AND WLz
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise AND is performed on multiple wordlines in the same NAND string
Result
Result
Activate WL
Activate WL
Activate WL

## Slide 64: Multi-Wordline Sensing (MWS)
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise OR is performed on wordlines from different NAND strings connected to the same bitline
WLi OR WLj OR WLk
BL1
⋯
WLi
1
⋯
⋯
WLk
1
⋯
Block Bl
Block Bn
⋯
WLj
0
⋯
Block Bm
Result

## Slide 65: Multi-Wordline Sensing (MWS)
Flash-Cosmos activates multiple wordlines simultaneously to perform multi-operand bulk bitwise operations
Bitwise OR is performed on wordlines from different NAND strings connected to the same bitline
BL1
⋯
WLi
1
⋯
⋯
WLk
1
⋯
Block Bl
Block Bn
⋯
WLj
0
⋯
Block Bm
1
BL activation
WLi OR WLj OR WLk
Result
Activate WL
Activate WL
Activate WL

## Slide 66: Flash-Cosmos Projects
Project 1: Logic optimization
  The goal is to optimize logic circuits based on the fact that large-input gates are possible and effective in Flash-Cosmos
Project 2: Technology mapping and analysis
  The goal is to map the logic to SSD blocks and pages.
  The input to this phase is the organization of the SSD and netlist of the logic
  Estimate latency

## Slide 67: Hybrid Storage System Simulator
Goal: Implement a hybrid storage system simulator with multiple storage devices
Extend the open-sourced codebase of Sibyl with simulated storage devices
Simulator should be aware of the characteristics of
  NAND flash memory (out-of-place write, write alignment, physical and logical units etc.)
  Device characteristics (capacity, I/O latency and endurance of the device)
The simulator should perform data placement and migration of pages on the simulated devices
Implement a simple I/O scheduling policy that considers the inter-request arrival time of requests

## Slide 68: Progressive Garbage Collection in MQSim
Goal: Implement a garbage collection policy in MQSim that does not interfere with the I/O requests
Current garbage collection (GC) policy in MQSim blocks I/O requests until it is completed
One approach,
  Perform garbage collection in multiple steps
  If there is an ongoing GC process and a new I/O request comes, MQSim should complete the current step and process the I/O request
Gives a good understanding of the GC process which is very critical to modern NAND flash memory devices

## Slide 69: Fine-grained Mapping in MQSim
Goal: Implement a finer granularity mapping policy in MQSim
Current logical-to-physical mapping of I/O requests is managed at page granularity (16KB)
  This wastes space if the size of write request is less than the page size
Implement a finer granularity mapping policy which can manage sub-pages (4KB or 8KB)
This reduces the fragmentation in flash pages and helps improve the performance with a minimal overhead
This project gives a good understanding of how FTL handles I/O requests in modern NAND flash devices

## Slide 70: Refactoring MQSim
Goal: Refactor MQSim codebase to make the simulator simple, readable and extensible while understanding the state-of-the-art SSD simulator
Refactor the code to
  Follow standard C++ coding guidelines (based on Google C++ Style Guide)
  Reduce the complexity of many features that currently use custom implementation by replacing with standard template libraries
  Improve the readability and extensibility by removing unused functions and headers
This project gives a good understanding of all components of MQSim and how they interact with each other